## Slide 1: REAL-TIME Storage and Demand Management
Jean-Yves Le Boudec (EPFL) ,
joint work with
Nicolas Gast (EPFL)
Alexandre Proutière (KTH)
Dan-Cristian Tomozei (EPFL)
Energy Systems Week: Management of Variability and Uncertainty in Energy Systems
April 2013, Newton Institute, Cambridge, UK

## Slide 2: INTroduction

## Slide 3: Storage and Demand Response can be used to mitigate volatility of renewables
Motivation: Swiss Nanotera grid (M. Kayal, M. Paolone) use of storage in active distribution network as in [Bianchi et al, 2012]
In this talk:
  can we use storage to compensate for renewable forecast errors ?
  can we control storage with prices ?
  can demand response substitute for storage ?

## Slide 4: USING STORAGE TO CopE with RENEWABLE Volatility
1.
[Bejan et al 2012] Bejan, Gibbens, Kelly, “Statistical aspects of storage systems modelling in energy networks,” 46th Annual Conference on Information Sciences and Systems 2012
[Gast et al 2012] Gast, Tomozei, Le Boudec. “Optimal Storage Policies with Wind Forecast Uncertainties”, GreenMetrics 2012
[Gast et al 2013] Gast, Tomozei, Le Boudec. “Optimal Energy Storage Policies with Renewable Forecast Uncertainties ”, submitted, 2013

## Slide 5: Production scheduling w. forecasts errors
Base load production scheduling
  Deviations from forecast
  Use storage to compensate
Social planner point of view
  Quantify the benefit of storage
  Obtain performance baseline
    what could be achieved
    no market aspects
Compare two approaches
  Deterministic approach
    try to maintain storage level at e.g. ½ of its capacity using updated forecasts
  Stochastic approach
    Use statistics of past errors.
Pump hydro, Cycle efficiency
renewables + storage
renewables
load

## Slide 6: Production scheduling with delays
1a. Forecast load and renewable suppy 1b. Schedule dispatchable production
2. Compensate deviations from forecast by charging / discharging from storage
renewables
load
stored energy
renewables
load
stored energy

## Slide 7: Full compensation of fluctuations by storage may not be possible due to power / energy capacity constraints
Fast ramping energy source ( rich) is used when storage is not enough to compensate fluctuation
Energy may be wasted when
  Storage is full
  Unnecessary storage (cycling efficiency
Control problem: compute dispatched power schedule to minimize energy waste and use of fast ramping
renewables
load
fast ramping
renewables
load
spilled energy

## Slide 8: Example of scheduling policy: Fixed Offset
Fixed Offset policy: means excess production (expect to store) means deficit of production (expect to draw from storage)
Planned
Actual
offset

## Slide 9: Example of scheduling policy: Fixed Level
target a fixed storage level (e.g. )
[Bejan et al 2012]
renewables
load
stored energy
target level
Planned
Actual
renewables
load
stored energy
target level

## Slide 10: Metric and performance (large storage)
Fast ramping energy sources ( rich) is used when storage is not enough to compensate fluctuation
Energy may be wasted when
  Storage is full
  Unnecessary storage (cycling efficiency
Can we do better?
How to compute optimal offset?
Questions:
Numerical evaluation: data from the UK
(BMRA data archive https://www.elexonportal.co.uk/)
National data (wind prod & demand)
3 years
Corrected day ahead forecast: MAE = 19%
AWP = average wind power
FO -200
FO +0
FO +200
Target=50%
Target=80%

## Slide 11: Fixed offset is optimal for large storage
  Let with
Theorem. If the forecast error is distributed as . Then:
  () is a lower bound: for any policy
  FO is optimal for large storage:
  The optimal offset is for u such that:
11
=
Uses distribution of error
Fixed reserve is Pareto-optimal
Target=50%
curve : Lower bound
Optimal fixed offset AWP
Target=80%
Problem solved for large capacity
What about small / medium capacity?
FO

## Slide 12: Scheduling Policies for Small Storage
Dynamic offset policy:
  choose offset as a function of forecasted storage level
Stochastic optimal control (general idea)
  Compute a value of being at storage level B
Computation of V: depends on problem
  Here: solution of a fixed point equation:
  Approximate dynamic programming if state space is too large
  Can be extended to more complicated state V(t,B,B’,…)
Instant cost (losses or fast-ramping energy)
Storage level at next time-slot
Expectation on possible errors

## Slide 13: Dynamic Offset outperforms other heuristics
Large storage capacity (=20h of average production of wind energy)
  Power = 30% of average wind power
  Fixed Offset & Dynamic offset are optimal
Small storage capacity (=3h of average production of wind energy)
  Power = 30% of average wind power
  DO is the best heuristic
Maintaining storage at fixed level: not optimal
  There exist better heuristics
Fixed storage level
Dynamic offset
Fixed storage level
Fixed Offset
Dynamic offset
Fixed offset
Lower bound

## Slide 14: Take Home Message
For “large” (i.e. one day) storage, there is an optimal value of fixed offset reserve, which can be computed from forecast error statistics
Can be used to dimension secondary reserve
FO = 2% AWP

## Slide 15: Prices AND STORAGE in Real-Time Electricity Markets
2.
[Gast et al 2013] Gast, Le Boudec, Proutière, Tomozei, “Impact of Storage on the Efficiency and Prices in Real-Time Electricity Markets”, ACM e-Energy 2013, Berkeley, May 2013

## Slide 16: Storage and Real Time Prices
Impact of volatility on prices in real time market is studied by Meyn and co-authors, e.g. [Cho and Meyn, 2010] I. Cho and S. Meyn Efficiency and marginal cost pricing in dynamic competitive markets with friction, Theoretical Economics, 2010
We add storage to the model
Q1: how does storage impact volatility ? what is the required storage capacity ?
Q2: does the market provide optimal control ?

## Slide 17: A Macroscopic Model of Real Time Market with Storage Extension of [Cho and Meyn 2010]
Control
Randomness
Supply
Demand
Ramping Constraint
Day ahead
Storage
extracted (or stored) power
Storage cycle efficiency (E.g. )
Storage constraints
Power Capacity
Energy Capacity
if
if 0
H: brownian motion

## Slide 18: Scenario A: Storage at Supplier
Consumer’s payoff
Supplier’s payoff
stochastic price process on real time market
Consumer
Supplier
buy
sell
satisfied demand
frustrated demand

## Slide 19: Definition of a Dynamic Competitive Equilibrium (Storage at Supplier) [Cho and Meyn 2010]
such that
  maximizes welfare ( = expected discounted payoff) of consumer
  maximizes welfare of supplier (given friction constraints) for the same price process
Without storage, there exists such an equilibrium [Cho and Meyn 2010]
Consumer
Supplier

## Slide 20: Scenario B: Storage at Consumer
Consumer’s payoff
Supplier’s payoff
Dynamic Competitive Equilibrium such that
  maximizes consumer’s welfare
  maximizes supplier’s welfare for the same price process
Consumer
Supplier

## Slide 21: Scenario C: Stand-Alone Storage Operator
Consumer’s payoff
Supplier’s payoff
Storage Op’s payoff
Dynamic Competitive Equilibrium such that
  maximizes consumer’s welfare
  maximizes supplier’s welfare
  maximizes storage op’s welfare
  for the same price process
Consumer
Supplier

## Slide 22: Dynamic Competitive Equilibria exist and are essentially the same for the 3 Scenarios [Theorem 3, Gast et al 2013]
1 u.e. = 360 MWh 1 u.p .= 600 MW = 0.6 GW2/h
2GW/h Cmax=Dmax= 3 u.p.

## Slide 23: Social Optimality
Assume a social planner wants to maximize total payoff
Total payoff is same for all 3 scenarios and is independent of price process
Structure of optimally social control Let optimal control is such that if ) increase (t) if ) decrease (t)

## Slide 24: The Social Welfare Theorem [Gast et al., 2013]
Any dynamic competitive equilibrium for any of the three scenarios maximizes social welfare

## Slide 25: The Invisible Hand of the Market may not be optimal
Any dynamic competitive equilibrium for any of the three scenarios maximizes social welfare
However, this assumes a given storage capacity.
Is there an incentive to install storage ?
No, stand alone operators or consumers have no incentive to install the optimal storage
Expected social welfare
Expected welfare of stand alone operator

## Slide 26: Scaling Laws
(steepness) being close to social welfare requires the optimal storage capacity
optimal storage capacity scales like increase volatility and rampup capacity by = increase storage by

## Slide 27: What this suggests about storage :
with a free and honest market, storage can be operated by prices
however, there may not be enough incentive for storage operators to install the optimal storage size
perhaps preferential pricing should be directed towards storage as much as towards PV

## Slide 28: A MODEL OF REAL TIME DEMAND RESPONSE
3.
[Le Boudec and Tomozei 2013] Le Boudec, Tomozei, “Stability of a stochastic model for demand-response”, Stochastic Systems 2013, also available at http://infoscience.epfl.ch/record/185991

## Slide 29: Issue with Demand Response: Grid Changes Load
Widespread demand response may make load hard to predict
renewables
load with demand response
«natural» load

## Slide 30: A Macroscopic Model of Demand Response
Returning Demand
Expressed
Demand
Frustrated
Demand
Satisfied
Demand
Evaporation
Control
Randomness
Supply
Natural Demand
Reserve
(Excess supply)
Ramping Constraint
Backlogged Demand
load is delayed
update term
Macroscopic Model of [Cho and Meyn 2010]
demand response

## Slide 31: We obtain a 2-d Markov chain on continuous state space
Returning Demand
Expressed
Demand
Frustrated
Demand
Satisfied
Demand
Evaporation
Control
Randomness
Supply
Natural Demand
Reserve
(Excess supply)
Ramping Constraint
Backlogged Demand

## Slide 32: The Control Problem
Control variable: production bought one time slot ago in real time market
Controller sees only supply and expressed demand
Our Problem: keep backlog stable
Ramp-up and ramp-down constraints

## Slide 33: Threshold Based Policies
Forecast supply is adjusted to forecast demand
R(t) := reserve = excess of demand over supply
Threshold policy:
if increase supply to come as close to as possible (considering ramp up constraint)
else decrease supply to come as close to as possible (considering ramp down constraint)

## Slide 34: Simulations (evaporation )
Reserve
Backlog

## Slide 35: Simulations (evaporation )
means returning load is, in average, less
Large excursions into negative reserve and large backlogs are typical and occur at random times
r*
1 time step = 10mn

## Slide 36: Large backlogs may occur within a day, at any time (when evaporation )
Typical delay 30 mn, all simulations with same parameters as previous slide,
Day 1
t = 40 mn
t = 400 mn
t = 1280 mn
t = 40 mn
t = 400 mn
t = 1280 mn
Day 2

## Slide 37: ODE Approximation () explain large excursions into positive backlogs
r*

## Slide 38: Simulations (evaporation )
Reserve
Backlog

## Slide 39: Simulations (evaporation )
means returning load is, in average, more
Backlog grows more rapidly
1 time step = 10mn

## Slide 40: ODE Approximation () shows backlog is unstable

## Slide 41: Findings : Stability Results
If evaporation is positive, system is stable (ergodic, positive recurrent Markov chain) for any threshold
If evaporation is negative, system unstable for any threshold
Delay does not play a role in stability
Nor do ramp-up / ramp down constraints or size of reserve

## Slide 42: What this suggests about Demand Response:
Positive evaporation is essential occurs with thermal loads, might not always occur for all load
Model suggests that large backlogs are possible and unpredictible
Backlogged load is a new threat to grid operation Need to measure and forecast backlogged load
load with demand response
«natural» load
renewables

## Slide 43: Thank You !
[Cho and Meyn, 2010] I. Cho and S. Meyn Efficiency and marginal cost pricing in dynamic competitive markets with friction, Theoretical Economics, 2010
[Bejan et al 2012] Bejan, Gibbens, Kelly, “Statistical aspects of storage systems modelling in energy networks,” 46th Annual Conference on Information Sciences and Systems 2012
[Gast et al 2012] Gast, Tomozei, Le Boudec. “Optimal Storage Policies with Wind Forecast Uncertainties”, GreenMetrics 2012
[Gast et al 2013] Gast, Tomozei, Le Boudec. “Optimal Energy Storage Policies with Renewable Forecast Uncertainties ”, submitted, 2013
[Gast et al 2013] Gast, Le Boudec, Proutière, Tomozei, “Impact of Storage on the Efficiency and Prices in Real-Time Electricity Markets”, ACM e-Energy 2013, Berkeley, May 2013
[Le Boudec and Tomozei 2013] Le Boudec, Tomozei, “Stability of a stochastic model for demand-response”, Stochastic Systems 2013, also available at http://infoscience.epfl.ch/record/185991
[Bianchi et al. 2012] Bianchi, Borghetti, Nucci, Paolone and Peretto, “A Microcontroller-Based Power Management System for Standalone Microgrids With Hybrid Power Supply”, IEEE Transactions on Sustainable Energy, 2012