## Slide 1: Stochastic Analysis of Real and virtual storage in the smart grid
Jean-Yves Le Boudec,
joint work with Nicolas Gast
Dan-Cristian Tomozei
I&C
EPFL
IEEE-Greencom keynote, Cyberspace, September 2012

## Slide 2: INTroduction
1.

## Slide 3: Renewable but non dispatchable
Wind and PV require some mechanisms to compensate non dispatchability
Source: «Battle of the grids», Greenpeace, Report 2011.
Notes: « I am 100% autonomous with my PV roof»

## Slide 4: Renewable Methods to Compensate for Fluctuations of PV and Wind
Dispatchable renewables
Storage
Demand Response
Notes: Nant de Dranse (VS) source: CREM

## Slide 5: A MODEL OF DEMAND RESPONSE
2.
Le Boudec, Tomozei, Satisfiability of Elastic Demand in the Smart Grid, Energy 2011 and ArXiv.1011.5606

## Slide 6: Demand Response
= distribution network operator may interrupt / modulate power
elastic loads support graceful degradation
Thermal load (Voltalis), washing machines (Romande Energie«commande centralisée») e-cars
Voltalis Bluepod switches off thermal load for 60 mn

## Slide 7: Issue with Demand Response: Grid Changes Load
Widespread demand response may make load hard to predict
load with demand response
«natural» load
renewables

## Slide 8: Our Problem Statement
Does demand response work ?
  Delays
  Returning load
Problem Statement Is there a control mechanism that can stabilize demand ?
We make a macroscopic model of a transmission grid with large penetration of
  Demand response
  Non dispatchable renewables
We leave out for now the details of signals and algorithms

## Slide 9: Starting Point: Macroscopic Model of Cho and Meyn [1], without Demand Response
Step 1: Day-ahead market
Forecast demand:
Forecast supply:
Step 2: Real-time market
Actual demand
Actual supply
nominal reserve
deterministic
random (deviation from forecast)
control (real time adjustement of
Generation)

## Slide 10: We add demand response to the model
We capture two effects of Demand Response
  Some load is delayed
  Returning load is modified
We do not model the IT aspects
  Operation of Demand response is instantaneous (but has delayed impact)
Notes: Different temperature conditions (inside, outside) when load returns
Different charging rate (resistive losses)

## Slide 11: Our Macroscopic Model with Demand Response
Returning Demand
Expressed
Demand
Frustrated
Demand
Satisfied
Demand
Evaporation
Control
Randomness
Supply
Natural Demand
Reserve
(Excess supply)
Ramping Constraint
Backlogged Demand

## Slide 12: Demand that was subject to demand response is later re-submitted
Delay term (time slots) is the average delay
Update term (evaporation): with or is the evaporation rate (proportion of lost demand per time slot)
Supply
Returning
Demand
Expressed
Demand
Frustrated
Demand
Satisfied
Demand
Backlogged Demand
Natural Demand
Evaporation
Control
Randomness
Reserve
(Excess supply)

## Slide 13: Deviations from Forecasts
Assumption : ARIMA(0, 1, 0) typical for deviation from forecast
S. Meyn
“Dynamic Models and Dynamic Markets
for Electric Power Markets”

## Slide 14: We obtain a 2-d Markov chain on continuous state space
Returning Demand
Expressed
Demand
Frustrated
Demand
Satisfied
Demand
Evaporation
Control
Randomness
Supply
Natural Demand
Reserve
(Excess supply)
Ramping Constraint
Backlogged Demand

## Slide 15: The Control Problem
Control variable: production bought one time slot ago in real time market
Controller sees only supply and expressed demand
Our Problem: keep backlog stable
Ramp-up and ramp-down constraints

## Slide 16: Threshold Based Policies
Forecast supply is adjusted to forecast demand
R(t) := reserve = excess of demand over supply
Threshold policy:
if increase supply to come as close to as possible (considering ramp up constraint)
else decrease supply to come as close to as possible (considering ramp down constraint)

## Slide 17: Simulations (evaporation )
Reserve
Backlog

## Slide 18: Simulations (evaporation )
means returning load is, in average, less
Large excursions into negative reserve and large backlogs are typical and occur at random times
r*
1 time step = 10mn

## Slide 19: Large backlogs may occur within a day, at any time (when evaporation )
Typical delay 30 mn, all simulations with same parameters as previous slide,
Day 1
t = 40 mn
t = 400 mn
t = 1280 mn
t = 40 mn
t = 400 mn
t = 1280 mn
Day 2

## Slide 20: ODE Approximation () explain large excursions into positive backlogs
r*

## Slide 21: Simulations (evaporation )
Reserve
Backlog

## Slide 22: Simulations (evaporation )
means returning load is, in average, more
Backlog grows more rapidly
1 time step = 10mn

## Slide 23: ODE Approximation () shows backlog is unstable

## Slide 24: Findings : Stability Results
If evaporation is positive, system is stable (ergodic, positive recurrent Markov chain) for any threshold
If evaporation is negative, system unstable for any threshold
Delay does not play a role in stability
Nor do ramp-up / ramp down constraints or size of reserve

## Slide 25: Evaporation
Negative evaporation means: delaying a load makes the returning load larger than the original one.
Could this happen ?
Q. Does letting your house cool down now imply spending more heat in total compared to keeping temperature constant ?
return of the load:
Q. Does letting your house cool down now imply spending more heat later ?
A. Yes (you will need to heat up your house later -- delayed load)

## Slide 26
Assume the house model of [6]
leakiness
inertia
heat provided
to building
outside

## Slide 27
efficiency
E, total energy provided
achieved
Scenario | Optimal | Frustrated
Building temperature |  | 
Heat provided |  | 
Scenario | Optimal | Frustrated
Building temperature |  | 
Heat provided |  | 

## Slide 28
Q. Does letting your house cool down now imply spending more heat in total compared to keeping temperature constant ?
A. No, less heat

## Slide 29: Findings
Resistive heating system: evaporation is positive.
This is why Voltalis bluepod is accepted by users
If heat = heat pump, coefficient of performance may be variable negative evaporation is possible
Electric vehicle: delayed charge may have to be faster, less efficient, negative evaporation is possible

## Slide 30: What this suggests about Demand Response:
Negative evaporation makes system unstable Existing demand-response positive experience (with Voltalis/PeakSaver) might not carry over to other loads
Model suggests that large backlogs are possible and unpredictible
Backlogged load is a new threat to grid operation Need to measure and forecast backlogged load
load with demand response
«natural» load
renewables

## Slide 31: USING STORAGE TO CopE with Wind Volatility
3.
Gast, Tomozei, Le Boudec. Optimal Storage Policies with Wind Forecast Uncertainties, GreenMetrics 2012

## Slide 32: Storage
Stationary batteries, pump hydro Cycle efficiency
renewables + storage
renewables
load

## Slide 33: Operating a Grid with Storage
1a. Forecast load and renewable suppy 1b. Schedule dispatchable production
2. Compensate deviations from forecast by charging / discharging from storage
renewables
load
stored energy
renewables
load
stored energy

## Slide 34: Full compensation of fluctuations by storage may not be possible due to power / energy capacity constraints
Fast ramping energy source ( rich) is used when storage is not enough to compensate fluctuation
Energy may be wasted when
  Storage is full
  Unnecessary storage (cycling efficiency
Control problem: compute dispatched power schedule to minimize energy waste and use of fast ramping
renewables
load
fast ramping
renewables
load
spilled energy

## Slide 35: Example: Wind data & forecasting
Aggregate data from UK (BMRA data archive https://www.elexonportal.co.uk/)
Demand perfectly predicted
3 years data
Scale wind production to 20% (max 26GW)
Relative error
Day ahead forecast = 24%
Corrected day ahead forecast = 19%

## Slide 36: Example: The Fixed Reserve Policy
Set to where is fixed (positive or negative)
Metric: Fast-ramping energy used (x-axis) Lost energy (y-axis) = wind spill + storage inefficiencies
Efficiency
Efficiency

## Slide 37: A lower bound
  Depends on storage characteristics
    Efficiency, maximum power (but not on size)
  Assumption valid if prediction is best possible
Theorem. Assume that the error
conditioned to is distributed as . Then:
(i)
where
(ii) The lower bound is achieved by the Fixed Reserve when storage capacity is infinite.

## Slide 38: Lower bound is attained for .
Efficiency
Efficiency

## Slide 39: The BGK policy [Bejan, Gibbens, Kelly 2012]
aims at keeping a constant level of stored energy
renewables
load
stored energy
target level
Is moderately sub-optimal for large energy storage capacity
BGK

## Slide 40: Small energy storage capacity?
BGK is far from lower bound – can one do better ?

## Slide 41: Scheduling Policies for Small Storage
Fixed Reserve:
BGK: compute so as to let storage level be close to nominal value
Dynamic Reserve: compute so as to minimize average anticipated cost
  Solved using an MDP model and policy iteration
renewables
load

## Slide 42: Dynamic Reserve uses a Control Law
  Effective algorithm to the Dynamic Reserve policy
Level of storage
Reserve
Level of storage
Reserve
Level of storage
Reserve
Level of storage
Reserve
Efficiency
Efficiency

## Slide 43: The Dynamic Reserve policies outperform BGK
  Trying to maintain a fixed level of storage is not optimal
BGK: maintain fixed storage lvl
Fixed Reserve
Lower bound
Dynamic reserve
Efficiency
Efficiency

## Slide 44: What this suggests about Storage
(BGK policy: ) Maintain storage at fixed level: not optimal
  Worse for low capacity
  There exist better heuristics
Lower bound (valid for any type of policy)
  depends on and maximum power
  Tight for large capacity (>50GWh)
  Still gap for small capacity
  50GWh and 6GW is enough for 26GW of wind
  Quality of prediction matters

## Slide 45: Conclusion: Demand Response vs Storage
Demand Response
Attractive (little capital investment)
Unpredictable effects
Storage
Capital investment
Can be managed and understood

## Slide 46: Questions ?
[1] Cho, Meyn – Efficiency and marginal cost pricing in dynamic competitive markets with friction, Theoretical Economics, 2010
[2] Le Boudec, Tomozei, Satisfiability of Elastic Demand in the Smart Grid, Energy 2011 and ArXiv.1011.5606
[3] Le Boudec, Tomozei, Demand Response Using Service Curves, IEEE ISGT-EUROPE, 2011
[4] Le Boudec, Tomozei, A Demand-Response Calculus with Perfect Batteries, WoNeCa, 2012
[5] Papavasiliou, Oren - Integration of Contracted Renewable Energy and Spot Market Supply to Serve Flexible Loads, 18th World Congress of the International Federation of Automatic Control, 2011
[6] David MacKay, Sustainable Energy – Without the Hot Air, UIT Cambridge, 2009
[7] Bejan, Gibbens, Kelly, Statistical Aspects of Storage Systems Modelling in Energy Networks. 46th Annual Conference on Information Sciences and Systems, 2012, Princeton University, USA.